# Flower Class Corvette

| Name |  | Turn | 7/15 cm | Weapons |  |
| --- | --- | --- | --- | --- | --- |
| Size Class | 3M | Acc + | 2 | A | 4” | FPS |  |  |
| ID |  | Dec - | 5 | Y | 2 lb (a) | APS |  |  |
| Max Speed | 20 | SLF | 1.5 | C | 20mm | FP |  |  |
|  | D | 20 mm | FS |  |  |
|  | DC | 40 |  |  |  |
| Damage Notes | CO |
|  | Helmsman |
|  | Engineer |

Original:

1939-1940 Programme:

Displacement: 950 tons  
Dimensions: 62.5 x 10.0 x 3.5 meters (205 x 33 x 11.5 feet)  
Propulsion: 2 fire tube Scotch boilers, 1 4-cyl. triple expansion steam engine, 2750 hp., 16 knots  
Range: 3500 nm. at 12 knots  
Crew: 85  
Radar: SW1C or 2C (later)  
Sonar: Type 123A, later Type 127DV  
Fire Control: 
EW: none  
Armament: 1 4" BL Mk.IX single, 2 .50 cal mg twin, 2 Lewis .303 cal mg twin, 2 Mk.II depth charge throwers, 2 depth charge rails, 40 depth charges.

Originally fitted with minesweeping gear, later removed.

1940-1041 Programme:

Propulsion: 2 water tube boilers, 1 4-cyl. triple expansion steam engine, 2750 hp., 16 knots

Final:

Crew: 95  
Radar: Type 271 surface/air, SW2C or 2CP air warning  
Sonar: Type 145  
Fire Control: 
EW: none  
Armament: 1 4" BL Mk.IX single, 1 2 Pdr. Mk.VIII single pom-pom, 2 20mm Oerlikon single, 1 Hedgehog ASW mortar (many), 4 MK.II depth charge throwers, 2 depth charge rails, 70 depth charges.

Ships assigned to Operations Torch and Neptune gained an extra two 20mm singles.